## Slide 1
OpenCellular - Mechanics Assembly Document
Date | Version | Change Note No./Notes
19-01-2017 | 0.1 | Initial draft
History

## Slide 2
OpenCellular - Assembly

## Slide 3
Main Chassis Sub Assembly
1.0

## Slide 4
1.1
Guide Pin
Main Chassis Sub Assembly
Mechanics Chassis Sub Assembly Sequence |  | 
Sequence | Assembly steps | Type of Assembly
1.1 | Guide pin (FPQSA4-P3.00-L4-B10 2nos.) would be assembled by chassis manufacturing vendor | Pre – Assembly (Vendor Supplied)

## Slide 5
1.2
Mechanics Chassis Sub Assembly Sequence |  | 
Sequence | Assembly steps | Type of Assembly
1.2 | Assemble Gaskets at 3 places as shown in above image 1. Main chassis gasket, 2. Front cover gasket & 3. Battery cover gasket Note: Gasket material B017XS7395-60 from Parker or Equivalent | Factory Assembly
Main chassis Gasket
Front cover Gasket
Battery cover Gasket
Main Chassis Sub Assembly

## Slide 6
Moist Vent
92005A320
Main Chassis Sub Assembly
Mechanics Chassis Sub Assembly Sequence |  | 
Sequence | Assembly steps | Type of Assembly
1.3 | Assemble Moist Vent (PMF100320 black) with torque of 0.7 +/- 0.1 Nm | Factory Assembly
1.4 | Assemble Grounding screw M5x10 (OpenCellular Part number 92005A320) hand tightened | Factory Assembly
1.3
1.4

## Slide 7
TIM
1.5
Main Chassis Sub Assembly
Mechanics Chassis Sub Assembly Sequence |  | 
Sequence | Assembly steps | Type of Assembly
1.5 | Assemble TIM (PG80A-00-150BL Fujipoly make) at 4 places as shown in above image | Factory Assembly

## Slide 8
1.6
Main Chassis Sub Assembly
Mechanics Chassis Sub Assembly Sequence |  | 
Sequence | Assembly steps | Type of Assembly
1.6 | Dispense Thermal Gel as shown in the above image (location of thermal gel are marked in Cyan color) Note: For detailed Thermal gel dispensing instruction refer drawing 291-000017 | Factory Assembly
Thermal Gel

## Slide 9
LED PCBA
1.7
Main Chassis Sub Assembly
Mechanics Chassis Sub Assembly Sequence |  | 
Sequence | Assembly steps | Type of Assembly
1.7 | Assemble LED PCB with M3x6 Screw & M3 washer at 5 places with torque of 1Nm | Factory Assembly
Screw & Washer

## Slide 10
1.8.a
Main Chassis Sub Assembly
Mechanics Chassis Sub Assembly Sequence |  | 
Sequence | Assembly steps | Type of Assembly
1.8 | Assemble RF Front end & RF SDR boards together & place it in the main chassis using guide pins for locating Assemble M3x6 screw 3 no's and M3 flat washers as shown (marked inside red circle) in the above image with torque of 1Nm | Factory Assembly
1.8.b

## Slide 11
1.9
Main Chassis Sub Assembly
Mechanics Chassis Sub Assembly Sequence |  | 
Sequence | Assembly steps | Type of Assembly
1.9 | Assemble Iridium module on to Sync board & ensure to fix firmly with M2x4 screw 2 places | Factory Assembly
1.10 | Align Sync board on to RF SDR board & fix the board firmly with M3x6 screw 2 places and M3 flat washers as shown in the above image (Marked in red circle) with torque of 1Nm | Factory Assembly
1.10
Iridium module
Iridium module
Sync Board

## Slide 12
1.11
Main Chassis Sub Assembly
Mechanics Chassis Sub Assembly Sequence |  | 
Sequence | Assembly steps | Type of Assembly
1.11 | Dispense Thermal Gel for RF FE Heat spreader plate as shown in the above image (location of thermal gel are marked in Cyan color) Note: For detailed Thermal gel dispensing instruction refer drawing 291-000019 | Factory Assembly
1.12 | Assemble Heat spreader plates on top of RF Front end & RF SDR boards Align the heat spreader plates and assemble M3x22 screw 12 no's and M3 flat washers as shown in the above image (Marked in red circle) with torque of 1Nm | Factory Assembly
1.12.a
1.12.b
RF SDR Heat spreader plate
RF FE Heat spreader plate
RF FE Heat spreader plate

## Slide 13
1.13
Main Chassis Sub Assembly
Mechanics Chassis Sub Assembly Sequence |  | 
Sequence | Assembly steps | Type of Assembly
1.13 | Assemble RF cable assembly – RF FE PCBA to RF SDR PCBA cable assembly 4 nos. as shown in above image | Factory Assembly
1.14 | Assemble GPS Antenna cable assembly (i.e., Stick GPS Antenna module at the location shown) & insert the connector inside the Grommet hole & connect to connector on RF SDR board as shown in above image | Factory Assembly
RF FE PCBA to RF SDR PCBA cable assembly
GPS Antenna cable assembly
1.14
GPS Antenna cable connector on RF SDR board

## Slide 14
1.15
Main Chassis Sub Assembly
1.16
Mechanics Chassis Sub Assembly Sequence |  | 
Sequence | Assembly steps | Type of Assembly
1.15 | Route Battery cable assembly as shown in the above image & insert one end of cable into battery compartment as shown | Factory Assembly
1.16 | Connect LED Cable assembly in LED board and Route LED cable assembly as shown in image | Factory Assembly

## Slide 15
Front Cover Sub Assembly
2.0

## Slide 16
2.1
Front Cover Sub Assembly Sequence |  | 
Sequence | Assembly steps | Type of Assembly
2.1 | Captive screw (PFC-2-M5-72) 2 no's , LED light pipe 14 no’s & overlay will be assembled by Front cover manufacturer | Pre – Assembly (Vendor Supplied)
Front Cover Sub Assembly
Captive screw
LED Light pipe
Front overlay

## Slide 17
2.2
Front Cover Sub Assembly Sequence |  | 
Sequence | Assembly steps | Type of Assembly
2.2 | Assemble Power switch cable assembly (Press fit) at the location shown in the above image | Factory Assembly
2.3 | Assemble Power connector cable assembly at the location shown in the above image with torque of 5Nm | Factory Assembly
Front Cover Sub Assembly
2.3
Power Switch cable assembly
Power connector cable assembly

## Slide 18
2.4
Front Cover Sub Assembly Sequence |  | 
Sequence | Assembly steps | Type of Assembly
2.4 | Assemble Antenna cable assembly at the location shown in the above image with torque of 0.7Nm to 1.1Nm | Factory Assembly
Front Cover Sub Assembly
Antenna Cable assembly

## Slide 19
Top Cover Sub Assembly
3.0

## Slide 20
3.1
Front Cover Sub Assembly Sequence |  | 
Sequence | Assembly steps | Type of Assembly
3.1 | Guide pin (FPQSA4-P3.00-L4-B10 2nos.) would be assembled by chassis manufacturing vendor | Pre – Assembly (Vendor Supplied)
Guide Pin
Top Cover Sub Assembly

## Slide 21
3.2
Front Cover Sub Assembly Sequence |  | 
Sequence | Assembly steps | Type of Assembly
3.2 | a) Assemble TIM (PG80A-00-150BL Fujipoly make) at 1 place as shown in above image | Factory Assembly
3.3 | Dispense Thermal Gel as shown in the above image (location of thermal gel are marked in Cyan color) Note: For detailed Thermal gel dispensing instruction refer drawing 291-000018 | Factory Assembly
Top Cover Sub Assembly
3.3
TIM

## Slide 22
3.4
Front Cover Sub Assembly Sequence |  | 
Sequence | Assembly steps | Type of Assembly
3.4 | Assemble Buzzer cable assembly with M1.6x6 Screw 2 no's with torque of 1Nm as shown in above image | Factory Assembly
Top Cover Sub Assembly
Buzzer cable assembly

## Slide 23
3.5
Front Cover Sub Assembly Sequence |  | 
Sequence | Assembly steps | Type of Assembly
3.5 | Assemble SODIMM module on GBC board & ensure it is firmly fixed with auto latch | Factory Assembly
Top Cover Sub Assembly

## Slide 24
3.6
Front Cover Sub Assembly Sequence |  | 
Sequence | Assembly steps | Type of Assembly
3.6 | Before placing GBC board on to Top cover connect buzzer cable assembly to its respective connector on GBC board | Factory Assembly
3.7 | Align GBC board with guide pins on top cover & assemble screws M3x6 Screw 8 nos. as shown in the above image (Marked in red circle) | Factory Assembly
Top Cover Sub Assembly
3.7

## Slide 25
3.8
Front Cover Sub Assembly Sequence |  | 
Sequence | Assembly steps | Type of Assembly
3.8 | Assemble mSATA at its respective position of connector & fix it firmly with M2x4 screw 1 nos. | Factory Assembly
Top Cover Sub Assembly
This image is only for reference

## Slide 26
4.1
Front Cover Sub Assembly Sequence |  | 
Sequence | Assembly steps | Type of Assembly
4.1 | Before assembling top cover on to Main chassis ensure to connect Batter cable assembly to GBC board Power switch cable assembly to GBC board LED Cable assembly to GBC board Power connector cable assembly to GBC board Antenna cable assembly to RF FE board | Factory Assembly
4.2 | Align Top cover & Main chassis assembly to their respective screw points & fix it firmly with M4x 10 screws 16 no’s with torque of 2.2 Nm | Factory Assembly
Main Chassis Assembly
4.1

## Slide 27
4.3
Front Cover Sub Assembly Sequence |  | 
Sequence | Assembly steps | Type of Assembly
4.3 | Align Front cover assembly on to Main chassis sub assembly & fix it firmly with M4x10 screw with torque of 2.2Nm as shown in above image (Marked in red circle) | Factory Assembly
Main Chassis Assembly

## Slide 28
4.4
Front Cover Sub Assembly Sequence |  | 
Sequence | Assembly steps | Type of Assembly
4.8 | Align battery cover & fix it firmly with M4x10 screws 6 nos. | Factory Assembly
Main Chassis Assembly

## Slide 29
Battery Assembly
Remove Battery cover from its place
Battery should be wrapped with foam & placed inside battery slot, before placing inside battery slot connectors need to be ensured to plugged
Reassemble Battery cover in its own place and assemble with the M4x6 screws with proper torque
Battery has to be assembled inside the unit during the field installation stage
Foam wrapped on top of battery
Battery placed inside battery compartment

## Slide 30
4.5
Front Cover Sub Assembly Sequence |  | 
Sequence | Assembly steps | Type of Assembly
4.5 | Align light pipe part on to front cover and fix it with 4 nos. of M3x6 screw as shown in above image (Marked in red circle) with torque of 1Nm | Factory Assembly
Main Chassis Assembly
Light pipe

## Slide 31
4.6
Front Cover Sub Assembly Sequence |  | 
Sequence | Assembly steps | Type of Assembly
4.6 | Align Shorty antenna plastic part and assemble the part with M3x6 screw with torque of 1 Nm | Factory Assembly
Main Chassis Assembly
Shorty Antenna

## Slide 32
Front Cover Sub Assembly Sequence |  | 
Sequence | Assembly steps | Type of Assembly
4.7 | Place the Main chassis assembly inside Front visual cover as shown & assemble 2 nos. of M4x10 screws & M3x6 screws 2 no’s at the location as shown. Assemble captive screws & M4x10 screw with torque of 2.2 Nm | Factory Assembly
Main Chassis Assembly
4.7

## Slide 33
4.8
Front Cover Sub Assembly Sequence |  | 
Sequence | Assembly steps | Type of Assembly
4.8 | Align Pole mounting bracket at the rear side of mechanics as shown & assemble 4 nos. of M5x10 Screw with torque of 4.5Nm | Factory Assembly
Main Chassis Assembly

## Slide 34
Pole mounting instructions
Pole clamp assembly
Pole clamp assembly first needs to be assembled to pole & then the unit with pole mounting bracket needs to be dropped & Wedge to be properly placed & tightened with screw
Wedge